## Slide 1: Computer Organization and Assembly Language
Amir Nawaz
Lecture 7

## Slide 2
Today we will learn?
Lea instruction
inc, dec,neg instructions
xcgh instruction

## Slide 3
LEA instruction
LEA stands for "Load Effective Address".
LEA is an assembly instruction that is used to store the effective memory address from an operand to a register.
For Example:
Lea dx,msg
Mov dx,offset msg

## Slide 4
INC instruction
INC instruction( add the value of 1 in the destination.)
Inc destination
Syntax:
For Example:
mov ax,1000H ; ax=1000H
Inc ax ;ax=1001H
Inc ax ;ax=1002H

## Slide 5
DEC instruction
DEC instruction( Subtract the value of 1 from the destination.)
mov ax,1000H ; ax=1001H
dec ax ;ax=1000H
dec ax ;ax=0FFFH
For Example:
dec destination
Syntax:

## Slide 6
NEG instruction
Reverses the sign of an operand.
Operand can be a register or memory operand.
.data
valB BYTE -1
valW WORD +32767
.code
mov al,valB ; AL = -1
neg al ; AL = +1
neg valW ; valW = -32767

## Slide 7
The XCHG instruction can swap two byte operands, two word operands, or two doubleword operands. The operands for the XCHG instruction may be two register operands, or a register operand with a memory operand.
For Example:
xchg ax,bx ;it will exchange the value of ax register with bx register
xchg var1,var2 ;it will exchange the value of var1 memory operand
with var2 memory operand
xchg ax,var1 ;it will exchange the value of ax register with var1 which is
a memory operand
XCHG instruction